## Slide 1
Microprocessor

## Slide 2
Intel 4004
1971
4 Bit Microprocessor
4kb Main Memory
45 Instruction
PMOS Technology
First Programmable Device In Calculators

## Slide 3
Intel 8008
1972
8 Bit Microprocessor
16 Kb Main Memory
48 Instruction
PMOS Technology
Slow

## Slide 4
Intel 8080
1973
8 Bit Microprocessor
64kb Main Memory
Two Microprocessor Clock Cycle Time
500000 Instruction Per Second
10x Faster Then 8008
Nmos Technology
Drawback Was That It Need Three Power Supplies
Small Computer Were Designed In Mid 1970 Using 8080 Cpu

## Slide 5
Intel 8085
1975
8 Bit Microprocessor
64kb Main Memory
1.3 Microprocessor Clock Cycle Time
246 Instruction
Intel Sold 100 Million Copies Of 8 Bit
Uses Only +5v Power Supply

## Slide 6
Intel 8086/8088
1978 for 8086 ,1979 for 8088
16 Bit Microprocessor
Data bus with 8086 16Bit and 8Bit for 8088
1 MB Main memory
400 Nano second clock cycle time
6 bytes instruction for 8086 and 4 bytes for 8088
More register and additional instruction
1981 personal computer for IBM

## Slide 7
Intel 80186
1982
16 Bit Microprocessor
1 MB Main memory
Contained special hardware like program counter and interrupt controller
Never used in PC
But was ideal for system that required a minimum of hardware

## Slide 8
Intel 80286
1983
16 Bit high performance microprocessor with memory management and protection
16 MB Main memory
Few additional instruction to handle extra 15MB
Instruction execution time 250 Nano second
Multitasking

## Slide 9
Intel 80386
1986
Intel first 32 bit
4 GB Main memory
Improvements include page handling in virtual environment
Includes hardware circuity for memory management and memory assignment
Memory paging and enhanced I/O permission

## Slide 10
Intel 80486
1989
32 bit high performance
4 GB Main memory
Incorporates 80387 floating point microprocessor and 8k byte cache
About half of instruction executed in 1 clock cycle instead of 20 n 80386

## Slide 11
Pentium
1993
32 bit microprocessor, 64 bit data bus, 36 bit address bus
64 GB Main memory
Double clocked 120 and 133 MHZ, dual integer processor
16 KB L1 cache (split instruction and data 8 KB each)

## Slide 12
Pentium Pro
1997
32 bit microprocessor, 64 bit data bus, 36 bit address bus, MMX
64 GB Main memory
32 KB split instruction / data L1 cache(16 KB each)
Module integrated 512 KB L2 cache(133 MHZ)
A version of P2 called Xeon, specifically designed for high end application

## Slide 13
Pentium II
1997
32 bit microprocessor, 64 bit data bus, 36 bit address bus,MMX
64 GB Main memory
32 KB split instruction / data L1 cache(16 KB each)
Module integrated 512 KB L2 cache(133 MHZ)
A version of P2 called Xeon, specifically designed for high end application

## Slide 14
Pentium III
1999
32 bit microprocessor, 64 bit data bus, 36 bit address bus
64 GB Main memory
Dual independent bus/ simultaneous
On chip 316

## Slide 15
Pentium IV
2002
32 bit microprocessor, 64 bit data bus, 36 bit address bus
64 GB Main memory